Physics 1 - F6 - 2018

How can random and Systematic errors be minimized during an experiment?

Estimate the precision to which the Young’s modulus, gamma of the wire can be determined from the formula gamma = ( 4 F l )/( pi d^2 e ) , given that the applied tension, F = 500 N, the length of the loaded wire, l=3 m, the diameter of the wire, d =1 mm, the extension of the wire, e = 5 mm and the errors associated with these quantities are 0.5 N, 2 mm, 0.01 mm and 0.1 mm respectively.

State the law of dimensional analysis.

If the speed V of the transverse wave along a wire of tension, T and mass, m is given by, V = sqrt{ T / m } . Apply dimensional analysis to check whether the given expression is correct or not.

Under what condition a passenger in a lift feels weightless?

Calculate the tension in the supporting cable of an elevator of mass 500 kg which was originally moving downwards at 4 m/s and brought to rest with constant acceleration at a distance of 20m.

The rotating blades of a hovering helicopter swept out an area of radius 2 m imparting a downward velocity of 8 m/s of the air displaced. Find the mass of a helicopter.

Compute the mass of water striking the wall per second when a jet of water with a velocity of 5 m/s and cross-sectional area of 3x10^{-2} m^2 strikes the wall at right angle losing its velocity to zero.

How does projectile motion differ from uniform circular motion?

A rifle shoots a bullet with a muzzle velocity of 1000 m/s at a small target 200 m away. How high above the target must the rifle be aimed so that the bullet will hit the target?
(i) Where does the object strike the ground when thrown horizontally with a velocity of 15m/s from the top of a 40m high building?
(ii) Find the speed of travel when a man jumps a maximum horizontal distance of 1 m spending a minimum time on the ground.

What is meant by the following terms as used in simple harmonic motion (S.H.M)?
(i) Periodic motion.
(ii) Oscillatory motion.

List four important properties of a particle executing simple harmonic motion (S.H.M).

Sketch a labeled graph that represents the total energy of a particle executing simple harmonic motion (S.H.M).

The periodic time of a body executing S.H.M is 4 seconds. How much time interval from time, t = 0 will its displacement be half its amplitude?

A satellite of mass 600kg is in a circular orbit at a height 2x10^6 km above the earth’s surface. Determine the:
(i) Orbital speed.
(ii) Gravitational potential energy.

What would happen if gravity suddenly disappears?

Two base of a mountain are at sea level where the gravitational field strength is 9.81 N/kg . If the value of gravitational field at the top of the mountain is 9.7 N/kg, calculate the height of the mountain above the sea level.

Why is flywheel designed such that most of its mass is concentrated at the rim? Briefly explain.

Estimate the couple that will bring the wheel to rest in 10 seconds when a grinding wheel of radius 40 cm and mass 3 kg is rotating at 3600 revolutions
per minute.

Why an ice skater rotates at relatively low speed when stretches her arms and a leg outward?

Calculate the moment of inertia of a sphere about an axis which is a tangent to its surface given that the mass and radius of the sphere are 10 kg and 0.2 m respectively.

Which type of thermometer is most suitable for calibration of other thermometers?

Why at least two fixed points are required to define a temperature scale?

List two qualities which makes a particular property suitable for use in practical thermometers.

Describe how mercury in glass thermometer could be made sensitive.

What is meant by triple point of water?

Evaluate the temperature in Kelvin if the pressure recorded by a constant volume gas thermometer is 6.8x10^4 N m^{-2} given that the pressure at triple point 273.16 K is 4.6x10^4 N m^{-2} .

One gram of water becomes 1671 cm^3 of steam at a pressure of 1 atmosphere. If the latent heat of vaporization at this pressure is 2256 J/g, determine the:
(i) external work done.
(ii) increase in internal energy

Why during emission of radiations from black body its temperature does not reach zero Kelvin?

A black ball of radius 1 m is maintained at a temperature of 30 degrees C . How much heat is radiated by the ball in 4 seconds?

What do you understand by the term node as applied to electric circuit?

Outline three important points which are usually referred as sign convection in solving Kirchhoff’s second law problems.

How is ohmic conductor differ from non-ohmic conductor? Give one example in each case.

Study the Figure below then find the reading on the high resistance voltmeter, V.
### insert Figure here ###

Why the emf of a cell is sometimes called a special terminal potential difference?

Calculate the current flowing in the circuit when three similar cells each of emf 1.5 V and internal resistance 0.3 ohms are connected in parallel across a 2 ohms resistor.

Mention four types of energy losses suffered by a transformer.

Why choke coil is preferred over resistance to control alternating current?

Identify two difficulties which would arise when two straight wires are used to transmit electricity direct from the source to the city station.

Explain what could be done to light a 30 V bulb from a 220 volt A.C supply?

A series LCR circuit with inductance, L=0.12 H , capacitance, C =480 nF and resistance, R=23 ohms is connected to a 230 V variable frequency supply. Determine the:
(i) Maximum current flowing in the circuit.
(ii) Source frequency for which the current is maximum.

List two chief properties of semiconductors.

Why is it easier to establish the current in a semiconductor than in an insulator?

State a condition that could be employed to make an insulator conduct some electricity.

Distinguish between conductors and semiconductors on the basis of their energy band structures.

What is meant by depletion layer as used in pn -junction device?

Describe the effect of applying a reverse bias to the junction diode.

Sketch the graph of transfer characteristic of a transistor.
State the significance of the slope from the graph above.

What is the basic condition for a transistor to operate properly as an amplifier?

Briefly explain how a junction transistor can be connected to act as a current operated device.

Why the magnitude of output frequency of a full wave rectifier is twice the input frequency?

Draw a simple basic transistor switching circuit diagram.

What is meant by a logic gate?

List three basic logic gates that make up all digital circuits.

Study the Figure below then answer the questions that follow.
### Insert Figure here ###
(i) Identify the logic gates marked R and S .
(ii) Write down the output at s , such that when P = 1 , Q = 1 and when P = 0 , Q=0 .

Obtain the truth table for the circuit shown in the Figure below.
### Insert Figure here ###

What is meant by solar constant?

List two factors on which the solar constant depends.

Give two advantages of photovoltaic system.

Briefly explain how photovoltaic cells work.

Estimate the maximum power available from 10 m^2 of solar panels. Calculate the volume of water per second which must pass through if the inlet and outlet temperature of the panels are at 10 degrees C and 60 degrees C respectively. (Assume the wave carries away energy at the same rate as the maximum power available)